## Slide 1: SG2000 PCB Layout Guide
Version: 0.2
Release date: 2022/09/13

## Slide 2
Outline
Checklist
Stackup
DDR 电源绕线
Serdes讯号绕线 - MIPI/USB/EPHY
Single-end讯号绕线 - GPIO/SDIO - EMMC/AUD/XTAL/WIFI
模拟/数字电源绕线 - VDDC -模拟IO电源

## Slide 3
SG2000 PCB Type
PCB 依照支持不同PKG型式, 分成以下PCB layout: (1) QFN PKG: SG2002, DDR3/DDR2 SIP on PKG (4-Layer/6-Layer PCB) (2) BGA PKG: SG2000, DDR2/DDR3 SIP on PKG (4-Layer/6-Layer PCB)
Layout rule 分成以下两部份: (1) DDR Layout rule (2 types) (2) Serdes/Single-end/Power Layout rule (common rule)
PKG型式与叠构相对应PCB layout rule如下:
Type | Stackup | DDR layout rule | Serdes/Single-end/Power Layout rule
QFN PKG | (1) 4-layer PCB (2) 6-layer PCB (真6层) | QFN 电源绕线 | 4-layer/6-layer (真6层) PCB layout rule (common rule)
BGA PKG | (1) 4-layer PCB (2) 6-layer PCB (真6层) | BGA 电源绕线 | 

## Slide 4
Checklist

## Slide 5
Checklist – Stackup – 4L-PCB/6L-PCB
No. | Rule | Description | Requirement | Check
1 | 4L-PCB 叠构要求 | 介电层/铜 厚度限制 | 1. 确认介电层厚度 – pp/core (1) pp<=5mils (Cu与pp 压合后, pp不含Cu的厚度) (2) L2/L3 Core 厚度>=25mils, 2. 每层Cu厚度1oz. | 
2 | 6L-PCB 叠构要求 | 介电层/铜 厚度限制 | 1. 确认介电层厚度 – pp/core (1) L1/L2, L3/L4, L5/L6: pp<=5mils (Cu与pp 压合后, pp不含Cu的厚度) (3) all core 厚度>11mils 2. 每层Cu厚度1oz. | 

## Slide 6
Checklist - Layout rule
No. | Rule | Description | Requirement | Check
1 | DDR routing | DDR3Q_1.5V rule | 1. 确认QFN PKG E-pad solder mask 覆盖区 (7.6x7.6mm2) 3 颗VIA 2. 建议贴上SOC PKG 下方DDR 走线/VIA/Cap layout | 
2 | MIPI routing | 表层/内层 阻抗控制 | 与PCB vendor 确认polar 结果: (1) 表层: Diff Coated Coplanar Strips with GND 1B (2) 内层: Diff Offset Coplanar Strips 1B1A | 
3 |  | 表层走线 Lane to lane NO GND shielding | Lane to lane NO GND shielding 走线长度<3.5mm | 
4 |  | BGA PKG, GND plane rule – 确保MIPI 讯号return path. | TX/RX在SOC ball下方GND plane预留3通道以上 | 
5 |  | Length matching rule | 确认TX/RX length matching | 
6 | USB | 表层/内层 阻抗控制 | 与PCB vendor 确认polar 结果: (1) 表层: Diff Coated Coplanar Strips with GND 1B (2) 内层: Diff Offset Coplanar Strips 1B1A | 
7 |  | Length matching rule | P/N length matching | 
8 | EPHY routing | 表层/内层 阻抗控制 | 与PCB vendor 确认polar 结果: (1) 表层: Diff Coated Coplanar Strips with GND 1B (2) 内层: Diff Offset Coplanar Strips 1B1A | 
9 |  | Length matching rule | P/N length matching | 

## Slide 7
No. | Rule | Description | Requirement | Check
10 | Single-end rule | 表层/内层 shielding rule | Shielding rule | 
11 | EMMC rule | 表层/内层 shielding rule | Shielding rule | 
12 | AUD rule | 表层 shielding rule | Shielding rule | 
13 | XTAL rule | 表层 shielding rule | Shielding rule | 
14 | RTC rule | 表层 shielding rule | Shielding rule | 
15 | WIFI_ANT rule | 表层阻抗控制 | 与PCB vendor 确认polar 结果: (1) 表层: Coated Coplanar Strips with GND 1B | 
16 | VDC rule | 1. 确认Cap数量与位置, VIA数量 2. 通道宽度 | 1. Rule1: (1) SOC/PMIC 处VIA 数量 (2) SOC处Cap pin VDDC/GND VIA rule 2. 通道宽度参照 rule2 3. 建议贴上SOC PKG 下方VDDC 走线/VIA/Cap layout | 
17 | Analog IO Power rule | 1. 线宽rule 2. 确认Cap数量与位置, VIA数量 | 1. Rule1: (1) SOC/PMIC 处VIA 数量 (2) SOC处Cap pin power/GND VIA rule 2. 通道宽度参照 rule2 3. 建议贴上SOC PKG 下方power走线/VIA/Cap layout | 
Checklist - Layout rule

## Slide 8: QFN Ball Map
MIPI
DDR
EPHY
USB
AUD
EMMC
SDIO
SDIO

## Slide 9: BGA Ball Map
MIPI
DDR
EPHY
USB
AUD
EMMC
SDIO
SDIO

## Slide 10
Stackup
QFN/BGA PKG: SG200X
4-layer/6-layer PCB

## Slide 11
PCB 4-Layer Stackup
叠构层数: 4层
叠构厚度: 1mm +/-10% <=厚度 <=1.6mm +/-10%
每层Cu采用1oz.
介电层厚度限制:
参考叠构
层号 | 材质 | 厚度限制
L1/L2 | Prepreg | <=5mils (Cu与pp 压合后, pp不含cu厚度)
L3/L4 |  | 
L2/L3 | Core | >=25mils

## Slide 12
PCB 6-Layer Stackup
叠构层数: 6层
叠构厚度: 1.2mm +/-10% <= 厚度 <=1.6mm +/-10%
每层Cu采用1oz.
介电层厚度限制:
参考叠构
层号 | 材质 | 厚度限制
L1/L2 | Prepreg | <=5mils (Cu与pp 压合后, pp不含cu厚度)
L5/L6 |  | 
L3/L4 |  | 
L2/L3 | Core | >=11mils
L4/L5 |  | 

## Slide 13
DDR 电源绕线 (DDR3_1.5V)
QFN PKG: SG2002
4-layer/6-layer PCB

## Slide 14
pp
pp
Core
QFN - 4L/6L-PCB DDR Layout
Stackup: (1) 4L-PCB: GND@L1/L2/L4 (plane), 6L-PCB: GND@L1/L2/L3/L4/L6 (plane) (2) 4L-PCB: DDR3_1.5V@L3 (shape), 6L-PCB: DDR3_1.5V@L4 (shape)
L1 GND
L2 : GND
L3 : DDR3_1.5V
4-Layers Stackup
L4 : GND
DDR3_1.5V@Top
4L-PCB: DDR3_1.5V@L3
6L-PCB: DDR3_1.5V@L4
DDR3_1.5V@Bottom
6-layers Stackup
pp
pp
Core
L1 GND
L2 : GND
L5 : GND
L6 : GND
pp
L4 : DDR3_1.5V
Core
L3 : GND
SOC
PMIC

## Slide 15
QFN - 4L/6L-PCB - DDR3_1.5V - Rule 1
Power | Layer | SOC VIA count | Layout rule
DDR3_1.5V | Top | (1) @E-pad 7.6x7.6mm2区域: VIA 数量: 3 (2) pin out区域: VIA 数量: 6 | (1) 覆盖Solder mask区域: E-pad 7.6x7.6mm2 (2) 非覆盖Solder mask区域: E-pad 6x6mm2 (3) 确认DDR3_1.5V SOC 端VIA数量
DDR3_1.5V@Top
SOC
E-pad aera 6x6mm2 (uncover solider mask)
E-pad aera 7.6x7.6mm2 (solider mask)
pin out区域

## Slide 16
QFN - 4L/6L-PCB – DDR3_1.5V - Rule 2
Power | Layer | Layout rule
DDR3_1.5V | 4L-PCB: DDR3_1.5V@L3 6L-PCB: DDR3_1.5V@L4 | DDR3_1.5V main route, (1) 确认SOC与PMIC处有下各6颗VIA (2) , 扣除破孔有效宽度: W1>=1.5mm, W2>=1.5mm
DDR3_1.5V@Top
4L-PCB: DDR3_1.5V@L3
6L-PCB: DDR3_1.5V@L4
SOC
PMIC
SOC区域VIA
PMIC区域 VIA
W1
W2

## Slide 17
QFN - 4L/6L-PCB - DDR3Q_1.5V - Rule 3
Power | Layer | DeCap@Dram area | Layout rule
DDR3Q_1.5V | Top/Bottom | DDR3Q_1.5V@Bottom: (1) 0402 0.1uF: C1/C2 (2) 0402 1uF: C3/C4 (3) 0402 4.7uF: C1 | (1) DDR3_1.5V VIA rule E-pad 区域 3 颗via紧连C1/C2/C3 Pin-out 区域 6颗 via紧连C4/C5 (1) GND VIA rule 确认每颗Cap旁至少1颗GND via
C5
C4
C1
C2
C3
E-pad 区域:3 vias
Pin-out 区域:6 vias
DDR3_1.5V@Top
DDR3_1.5V@Bottom

## Slide 18
QFN - 4L/6L-PCB - DDR3_1.5V - Rule 4
DDR3_1.5V@Top
Power | PMIC 分支点 VIA 数量
DDR3_1.5V | (1) DDR3_1.5V: VIA 数量>=6 (2) GND: VIA 数量>=5
PMIC
PMIC routing area
PMIC 分支点 VIA 数量
DDR3_1.5V:
VIA 数量6
GND:
VIA 数量5

## Slide 19
DDR 电源绕线 (DDR3_1.5V)
BGA PKG: SG2000
4-layer/6-layer PCB

## Slide 20
pp
pp
Core
BGA – 4L/6L-PCB DDR Layout
Stackup: (1) 4L-PCB: GND@L1/L2/L4 (plane), 6L-PCB: GND@L1/L2/L3/L4/L6 (plane) (2) 4L-PCB: DDR3_1.5V@L3 (shape), 6L-PCB: DDR3_1.5V@L4 (shape)
L1 GND
L2 : GND
L3 : DDR3_1.5V
4-Layers Stackup
L4 : GND
DDR3_1.5V@Top
4L-PCB: DDR3_1.5V@L3
6L-PCB: DDR3_1.5V@L4
DDR3_1.5V@Bottom
6-layers Stackup
pp
pp
Core
L1 GND
L2 : GND
L5 : GND
L6 : GND
pp
L4 : DDR3_1.5V
Core
L3 : GND
SOC
PMIC

## Slide 21
BGA – 4L/6L-PCB - DDR3_1.5V - Rule 1
Power | Layer | SOC VIA count | Layout rule
DDR3_1.5V | Top | (1) DDR3_1.5V (ball N5): 1 (2) DDR3_1.5V (merge ball): 4 | (1) 确认DDR3_1.5V SOC 端VIA数量 (2) Ball N5 VIA: 连接bottom Cap (3) Merge ball VIA: 连接内层main route trace
DDR3_1.5V (ball N5)
DDR3_1.5V (merge ball)
DDR3_1.5V@Top

## Slide 22
BGA – 4L/6L-PCB - DDR3_1.5V - Rule 2
Power | Layer | Layout rule
DDR3_1.5V | 4L-PCB: DDR3_1.5V@L3 6L-PCB: DDR3_1.5V@L4 | DDR3_1.5V main route: (1) 确认SOC处有下4颗VIA, PMIC处有下大于等于5颗VIA (2) 扣除破孔有效宽度: W1>=1.5mm, W2>=1.5mm
DDR3_1.5V@Top
4L-PCB: DDR3_1.5V@L3
6L-PCB: DDR3_1.5V@L4
SOC
PMIC
SOC区域VIA
PMIC区域 VIA
W1
W2
SOC

## Slide 23
BGA – 4L/6L-PCB - DDR3Q_1.5V - Rule 3
Power | Layer | DeCap@Dram area | Layout rule
DDR3Q_1.5V | Top/Bottom | DDR3Q_1.5V@Top: (1) 0402 1uF: C1/C2 DDR3Q_1.5V@Bottom: (1) 0402 0.1uF: C4/C5 (2) 0402 1uF: C3/C7/C6 (3) 0402 4.7uF: C8 | (1) DDR3_1.5V VIA rule 确认每颗Cap旁至少1颗DDR3_1.5V via (2) GND VIA rule 确认每颗Cap旁至少1颗GND via
DDR3_1.5V@Top
DDR3_1.5V@Bottom
DDR3_1.5V (ball N5)
DDR3_1.5V (merge ball)
C4
C6
C7
C8
C3
C5
C1
C2

## Slide 24
BGA – 4L/6L-PCB - DDR3_1.5V - Rule 4
DDR3_1.5V@Top
Power | PMIC 分支点 VIA 数量
DDR3_1.5V | (1) DDR3_1.5V: VIA 数量>=6 (2) GND: VIA 数量>=5
PMIC
PMIC routing area
PMIC 分支点 VIA 数量
DDR3_1.5V:
VIA 数量6
GND:
VIA 数量5

## Slide 25
Serdes 讯号绕线
QFN/BGA PKG: SG200X
4-layer/6-layer PCB

## Slide 26
QFN/BGA – 4L/6L-PCB- MIPI Routing – 表层走线 Option1 Rule 1
Signal | Layer | Zo | Trace width/spacing (mm) | Shielding Rule
MIPI_TX/RX Diff pair | Top/ Bottom | 100 ohm | 0.125/0.125/0.15 (W/S/D) | Lane to Lane GND shielding
QFN MIPI TX/RX differential signals layout@Top
BGA MIPI TX/RX differential signals layout@Top
SOC
MIPI_RX
MIPI_TX
MIPI TX/RX
SOC
MIPI_RX
MIPI_TX

## Slide 27
QFN/BGA – 4L/6L-PCB – MIPI Routing – 表层走线 Option1 - Rule 2
Signal | Layer | Requirement | Layout Rule
MIPI_TX/RX Diff pair | Top/ Bottom | Lane to lane shielding GND VIA distance | L1 (GND stitching VIA) < 7.5mm NO GND shielding length L2 < 3.5mm
BGA MIPI TX/RX shielding GND VIA distance@Top
L1
QFN MIPI TX/RX shielding GND VIA distance@Top
SOC
SOC
L1
L2
L2

## Slide 28
QFN/BGA – 4L/6L-PCB – MIPI Routing – 表层走线 Option2 - Rule
Signal | Layer | Zo | Trace width/spacing (mm) | Shielding Rule
MIPI_TX/RX Diff pair | Top/ Bottom | 100ohm | 0.125/0.125/0.3/0.3 (W/S/Ds/Dg) | (1) Lane to Lane NO GND shielding, 确认diff底下GND plane完整 (2) TX/RX Group GND shielding, GND shielding必须下VIA: VIA to VIA 距离<7.5mm (3) Lane to lane 距离限制: 1) 绕线长度>=10mm, Ds=3W, Dg=3W (可允许Dg=2W) 2) 绕线长度<10mm, Ds>=2W, Dg>=2W
MIPI TX
MIPI RX

## Slide 29
Signal | Layer | Zo (ohm) | Trace width/spacing (mm) (W/S/Ds/Dg) | Shielding Rule
MIPI_TX/RX Diff pair | 4L-PCB: L2 6L-PCB: L3 | 100 | 4L-PCB: 0.125/0.25/0.3/0.3 6L-PCB: 0.125/0.25/0.3/0.3 | (1) Lane to Lane NO GND shielding, 确认diff底下 GND plane完整 (2) TX/RX Group GND shielding, GND shielding必须下VIA: VIA to VIA 距离<7.5mm (3) Lane to lane 距离限制: 1) 绕线长度>=10mm, Ds=3W, Dg=3W (可允许Dg=2W) 2) 绕线长度<10mm, Ds>=2W, Dg>=2W
QFN/BGA – 4L/6L-PCB – MIPI Routing – 内层走线 - Rule
SOC
RX@内层, Option2, RX group GND shielding
MIPI_RX
MIPI TX
GND
MIPI RX
GND

## Slide 30
DQ/CA@L1
BGA – 4L/6L-PCB – MIPI Routing – GND Plane Rule
MIPI TX/RX@Top + GND plane@L2
MIPI TX/RX@Top
SOC
GND plane 保留3个通道以上
Signal | Layer | Layout rule
TX/RX GND plane | L2 | 确认TX/RX@SOC 下方GND plane@L2 的破孔会保留3组通道以上 (Layer2 GND plane 请参照下图)
MIPI_RX
MIPI_TX
GND VIA
1
2
3

## Slide 31
MIPI Routing – Length Matching Rule
Signal | Matching Reference | Matching Length
TX | inter skew | <=2.5mm (100mils)
RX | inter skew | 
TX | P/N intra skew | <=0.5mm (20mils)
RX | P/N intra skew | 

## Slide 32
QFN/BGA – 4L/6L-PCB – USB Routing – 表层走线- Rule
Signal | Layer | Zo | Trace width/spacing (mm) | Shielding Rule
USB Diff pair | Top/ Bottom | 90ohm | 0.125/0.1/0.15 (W/S/D) | Lane to lane GND shielding. Shielding GND VIA: Lane to Lane GND shielding必须下VIA (VIA to VIA 距离<=7.5mm)
Shielding GND VIA
S1
GND
GND
Diff P/N
USB Diff pair
pp
GND
G
G
P
N
W
W
S
D
D

## Slide 33
QFN/BGA – 4L/6L-PCB – USB Routing – 内层走线- Rule
Signal | Layer | Zo | Trace width/spacing (mm) | Shielding Rule
USB Diff pair | 4L-PCB: L2 6L-PCB: L3 | 90ohm | 4L-PCB: 0.125/0.175/0.15 (W/S/D) 6L-PCB: 0.125/0.175/0.15 (W/S/D) | Lane to lane GND shielding. Shielding GND VIA: Lane to Lane GND shielding必须下VIA (VIA to VIA 距离 S1<=7.5mm)
USB Diff pair
Shielding GND VIA
S1
GND
GND
Diff P/N

## Slide 34
USB Routing – Length Matching Rule
Signal | Matching Reference | Matching Length
USB_DM USB_DP | P/N intra skew | <=0.5mm (20mils)

## Slide 35
QFN/BGA – 4L/6L-PCB - EPHY Routing – 表层走线 - Rule1
Signal | Layer | Zo | Trace width/spacing (mm) | Shielding Rule
EPHY TX/RX Diff pair | Top | No control | 0.125/0.125/0.125 (Ws/Sg/Wg) | P/N 之间须有GND trace shielding TX/RX 之间须有GND trace shielding GND trace VIA rule: 1) 需确认靠近SOC端的GND trace 至少有一颗VIA与SOC PKG GND 构成回路 2) 需确认靠近transformer端的GND trace至少有一颗VIA与transformer GND pin构成回路
EPHY TX/RX
Core
GND
P
N
Ws
Ws
Sg
Sg
G
G
Sg
Sg
G
Wg
Wg
Wg
G
Shielding GND VIA
SOC
GND 回流VIA

## Slide 36
Signal | Layer | Requirement | Layout Rule
EPHY TX/RX | Top | TX to RX GND shielding 0.125/0.125 (Wg/Sg) | GND trace VIA rule: 1) 需确认靠近SOC端的GND trace 至少有一颗VIA与SOC PKG E-pad构成回路 2) 需确认靠近transformer端的GND trace至少有一颗VIA与transformer GND pin构成回路
QFN/BGA – 4L/6L-PCB - EPHY Routing – 表层走线 - Rule2
EPHY TX/RX Isolation
Core
GND
P
N
G
G
Sg
G
Wg
P
N
Sg
G
G
TX
RX

## Slide 37
EPHY Routing – Length Matching Rule
Signal | Matching Reference | Matching Length
EPHY TX/RX Diff pair | P/N intra skew | <=0.5mm (20mils)

## Slide 38
Single-end 讯号绕线
QFN/BGA PKG: SG200X
4-layer/6-layer PCB

## Slide 39
QFN/BGA – 4L/6L-PCB - Single-end – Rule
Signal | Layer | Shielding Rule | Trace width/spacing (mm)
SDIO RTC | 4L-PCB: Top/Bottom/L3 6L-PCB: Top/Bottom/L3 | Break out (fan-out) region: NO GND trace shielding, ref GND plane | W>=0.1 0.1/0.1 (S/D) (0.1mm spacing)
 |  | Main rout: NO GND trace shielding, ref GND plane | W>=0.1 0.15/0.1 (S/D) (0.15mm spacing)
pp
GND
G
S
S
W
W
S
D
S
W
S
S
W
G
D
…
NO GND trace shielding

## Slide 40
QFN/BGA - 4L/6L-PCB– EMMC – Rule
pp
GND
G
S
S
W
W
S
D
S
W
S
S
W
G
D
…
Signal | Layer | Shielding Rule | Trace width/spacing (mm)
EMMC_CLK EMMC_CMD EMMC_RST_N (BGA) | 4L-PCB: Top/Bottom/L3 6L-PCB: Top/Bottom/L3 | Break out (fan-out) region: NO GND trace shielding, ref GND plane | (1) W>=0.1 (2) 0.1/0.1 (S/D)
 |  | per trace shielding, ref GND plane | (1) W>=0.1 (2) D=0.1
Signal | Layer | Shielding Rule | Trace width/spacing (mm)
EMMC D0~D3 | Top | Break out (fan-out) region: NO GND trace shielding, ref GND plane | (1) W>=0.1 (2) 0.1/0.1 (S/D) (0.1mm spacing)
 |  | Main rout: NO GND trace shielding, ref GND plane | W>=0.1 0.15/0.1 (S/D) (0.15mm spacing)
pp
GND
G
G
S
W
D
D
Per trace shielding
NO GND trace shielding

## Slide 41
QFN 4L/6L-PCB – AUD – Rule
Signal | Layer | Shielding Rule | Trace width/spacing (mm)
AUD_MIC_L AUD_MIC AUD_OUT | Top | (1) per trace shielding (2) ref AUD GND plane (3) 确认AUD 讯号线下方有 完整AUD GND plane | W>=0.1 D=0.1
AUD@Top
pp
AUD GND
G
G
S
W
D
D
Per trace shielding
AUD GND
pin
AUD GND
AUD GND
AUD@L1/L2

## Slide 42
BGA – 4L/6L-PCB – AUD – Rule
Signal | Layer | Shielding Rule | Trace width/spacing (mm)
AUD_MIC_L/AUD_MIC_R AUD_MICL/AUD_MICR AUD_AOUTL/AUD_AOUR AC_AOUTL/AC_AOUR | Top | (1) per trace shielding (2) ref AUD GND plane (3) 确认AUD 讯号线下方有完整AUD GND plane | W>=0.1 D=0.1
AUD@Top
pp
AUD GND
G
G
S
W
D
D
Per trace shielding
AUD@L1/L2
AUD GND ball
AUD GND
AUD GND

## Slide 43
QFN/BGA – 4L/6L-PCB – XTAL_IN/OUT - Rule
Signal | Layer | Shielding Rule | Trace width/spacing (mm)
SYS_XTAL_IN SYS_XTAL_OUT | Top | per trace shielding ref GND plane | 0.25/0.25 (W/D)
XTAL_IN
XTAL_OUT
XTAL IC
pp
GND
G
G
S
W
D
D
Per trace shielding
BGA XTAL@Top
QFN XTAL@Top

## Slide 44
BGA only – 4L/6L-PCB – RTC_XIN/XOUT - Rule
Signal | Layer | Shielding Rule | Trace width/spacing (mm)
RTC_IN RTC_OUT | Top | 电容 to XTAL: per trace shielding | 0.25/0.1 (W/D)
pp
GND
G
G
S
S
W
W
S
D
D
Two trace shielding
XTAL@L1
pp
GND
G
G
S
W
D
D
Per trace shielding
XTAL
SOC
RTC_XIN
RTC_XOUT

## Slide 45
QFN/BGA – 4L/6L-PCB – WIFI_ANT Layout Rule
Signal | Layer | Zo | Shielding Rule | Trace width/spacing (mm)
WIFI_ANT | Top | 50ohm | Per trace shielding | 0.75/0.15/0.3 (W/D1/D2)
WIFI_ANT@Top
WIFI_ANT@GND/PWR plane
WIFI_ANT
WIFI_ANT 下方plane
需挖空
6L PCB
pp
GND
G
G
Sig
W
D1
D1
L1
L2
Core
GND
L3
GND
pp
L4
D2
D2
GND
L5
Core
PWR
PWR
GND
GND
4L-PCB

## Slide 46
模拟/数字电源绕线
QFN PKG: SG2002
4-layer/6-layer PCB

## Slide 47
QFN – 4L/6L-PCB – VDDC – Rule 1
Power | Layer | SOC VIA count | DeCap | Layout rule
VDDC | Top/Bottom | 10 | (1) 0402 0.1uF: C1/C2/C6/C8/ (2) 0402 1uF: C3/C4/C9 (3) 0402 4.7uF: C5/C7 | VDDC VIA rule 1) 每根VDDC pin 需连接两颗VIA 2) 确认每颗Cap旁至少1颗VDDC via (2) GND VIA rule 确认每颗Cap旁至少1颗GND via
VDDC@Top
VDDC@Bottom
SOC
C5
C7
C4
C8
C9
C1
C2
C3
C6

## Slide 48
QFN – 4L/6L-PCB – VDDC – Rule 2
VDDC@Top
4L-PCB: VDDC@L3
6L-PCB: VDDC@L4
SOC
PMIC
PMIC区域
W4
W2
Power | Layer | Layout rule
VDDC | VDDC main routing, 4L-PCB: DDR3_1.5V@L3 6L-PCB: DDR3_1.5V@L4 | DDR3_1.5V 内层绕线: (1) 确认SOC处10颗VIA, PMIC处6颗VIA (2) SOC区域扣除破孔有效宽度: W1>=4mm (SOC QFN正下方), W2>=1.5mm (进入SOC 区域) (3) PMIC区域扣除破孔有效宽度: W3>=1.5mm (4) Main route 扣除破孔有效宽度 : W4>=1.5mm
W3
SOC区域
W1
SOC处10颗VIA
PMIC处6颗VIA

## Slide 49
QFN – 4L/6L-PCB – VDDC – Rule 3
Power | PMIC 分支点 VIA 数量
VDDC | (1) VDDC: VIA 数量>=6 (2) GND: VIA 数量>=5
PMIC
PMIC routing area
PMIC 分支点 VIA 数量
VDDC:
VIA 数量6
GND:
VIA 数量6
VDDC@Top

## Slide 50
QFN – 4L/6L-PCB – Analog IO Power – Rule 1
Power | Layer | Layout rule
VDD18A_AUD/VDD_18A_MIPI VDD18A_USB_PLL_ETH VDD33A_EPH_USB VDDIO_RTC VDDIO_SD0_A/VDDIO_SD1 | 4L-PCB: Top/Bottom/L3 6L-PCB: Top/Bottom/L4 | @Top: (1) Break out (fan-out):线宽 W1>=0.25mm (2) Main route:线宽 W2>=0.5mm @内层 : 所有线宽 W3>=0.5mm @Bottom:所有线宽 W4>=0.5mm
Analog IO power@Top
Analog IO power@Bottom
Analog IO power@内层
SOC
SOC
W1
W4
W2
W3
W1

## Slide 51
QFN – 4L/6L-PCB – Analog IO Power – Rule 2
Power | Layer | Layout rule
VDD18A_AUD/VDD_18A_MIPI VDD18A_USB_PLL_ETH VDD33A_EPH_USB VDDIO_RTC VDDIO_SD0_A/VDDIO_SD1 | Top/Bottom | (1) Analog IO power VIA rule 确认每颗Cap旁至少1颗analog IO power via (2) GND VIA rule 确认每颗Cap旁至少1颗GND via
Analog IO power@Top
Analog IO power@Bottom
SOC

## Slide 52
模拟/数字电源绕线
BGA PKG: SG2000
4-layer/6-layer PCB

## Slide 53
BGA – 4L/6L-PCB – VDDC – Rule 1
Power | Layer | SOC VIA count | DeCap | Layout rule
VDDC | Top/Bottom | 9 | (1) 0402 0.1uF: C1 (2) 0402 1uF: C3/C4/C5 (3) 0402 4.7uF: C2 | VDDC VIA rule 确认VDDC via紧连CAP (2) GND VIA rule 确认GND via紧连CAP
SOC
VDDC@Top
VDDC@Bottom
C1
C2
C3
C4
C5

## Slide 54
BGA – 4L/6L-PCB – VDDC – Rule 2
Power | Layer | Layout rule
VDDC | VDDC main routing, 4L-PCB: DDR3_1.5V@L3 6L-PCB: DDR3_1.5V@L4 | DDR3_1.5V 内层绕线; (1) 确认SOC处9颗VIA, PMIC处6颗VIA (2) SOC区域,扣除破孔有效宽度: W1>=1mm (SOC ball 正下方), W2>=1.5mm (进入SOC 区域) (3) PMIC区域, 扣除破孔有效宽度: W3>=1.5mm (4) Main route, , 扣除破孔有效宽度: W4>=1.5mm
DDR3_1.5V@Top
4L-PCB: DDR3_1.5V@L3
6L-PCB: DDR3_1.5V@L4
SOC
PMIC
SOC区域
PMIC区域
W4
W2
W3
W1
SOC处9颗VIA
PMIC处6颗VIA

## Slide 55
BGA – 4L/6L-PCB – VDDC – Rule 3
Power | PMIC 分支点 VIA 数量
VDDC | (1) VDDC: VIA 数量>=6 (2) GND: VIA 数量>=5
PMIC
PMIC routing area
PMIC 分支点 VIA 数量
VDDC:
VIA 数量6
GND:
VIA 数量5
DDR3_1.5V@Top

## Slide 56
BGA – 4L/6L-PCB – Analog IO Power – Rule 1
Power | Layer | Layout rule
VDDIO_18A/VDDIO18_1 VDD18A_AUD/VDD18A_ETH/VDD_18A_MIPI VDD18A_PLL_N/VDD18A_USB VDD33A_EPHY/VDD33A_ETH VDDIO_EMMC/VDDIO_RTC/VDDIO_VIVO VDDIO_SD0/VDDIO_SD0_A/VDDIO_SD1 VDD09A_EPHY/VDD09A_MIPI VIN3V | 4L-PCB: Top/Bottom/L3 6L-PCB: Top/Bottom/L4 | @Top: 线宽 W1>=0.3mm (ball与VIA最短距离连线) @内层 : (1) SOC ball 区域: 线宽 W2>=0.3mm (2) SOC ball 以外区域: 线宽 W3>0.5mm @Bottom: (1) SOC ball 区域: 线宽 W4>=0.3mm (2) SOC ball 以外区域: 线宽 W5>0.5mm
Analog IO power@Top
Analog IO power@Bottom
Analog IO power@内层
SOC
SOC
W2
SOC ball 以外区域
SOC bal区域
W4
W5
SOC ball 以外区域
SOC
SOC bal区域
W3
W1

## Slide 57
BGA – 4L/6L-PCB – Analog IO Power – Rule 2
Power | Layer | Layout rule
VDDIO_18A/VDDIO18_1 VDD18A_AUD/VDD18A_ETH/VDD_18A_MIPI VDD18A_PLL_N/VDD18A_USB VDD33A_EPHY/VDD33A_ETH VDDIO_EMMC/VDDIO_RTC/VDDIO_VIVO VDDIO_SD0/VDDIO_SD0_A/VDDIO_SD1 VDD09A_EPHY/VDD09A_MIPI VIN3V | Top/Bottom | (1) Analog IO power VIA rule 确认每颗Cap旁至少1颗analog IO power via (2) GND VIA rule 确认每颗Cap旁至少1颗GND via
Analog IO power@Top
Analog IO power@Bottom
SOC

## Slide 58
Appendix

## Slide 59
MIPI/EPHY/USB/Antenna 阻抗控制
4-layer PCB

## Slide 60
MIPI/EPHY/USB 阻抗控制 –表层走线 Option1
Layer | Target Z (ohm) | W (mils) | S (mils) | D (mils) | Estimated Z (ohm)
Top/Bottom | 100 | 5 | 5 | 6 | 97.99
 | 90 | 5 | 4 | 6 | 92.48
MIPI/USB differential signals are required impedance control - Target impedance: (1) MIPI- CSI/DSI: 100ohm (2)USB: 90ohm
Differential signals shielding rule:
- pair to pair GND shielding
pp
GND
G
G
P
N
W
W
S
D
D

## Slide 61
Target Z (ohm) | W (mils) | S (mils) | D (mils) | Estimated Z (ohm)
100 +/- 5% | 5 | 5 | 6 | 97.99
Target Z | W (mils) | S (mils) | D (mils) | Estimated Z (ohm)
90 +/- 5% | 5 | 4 | 6 | 92.48
MIPI/EPHY/USB 阻抗控制 –表层走线 Option1

## Slide 62
MIPI 阻抗控制 – 表层走线 Option2
Layer | Target Z (ohm) | W (mils) | S (mils) | Ds (mils) | Dg (mils) | Estimated Z (ohm) | Rule
Top/Bottom | 100 | 5 | 5 | 12 | 12 | 99.96 | Ds=3W, Dg=3W
pp
GND
G
P
N
W
W
S
Ds
Dg
G
P
N
W
W
S
Dg

## Slide 63
Target Z (ohm) | W (mils) | S (mils) | Ds (mils) | Dg (mils) | Estimated Z (ohm)
100 +/- 5% | 5 | 5 | 12 | 12 | 99.96
 | 4 | 4 | 12 | 12 | 101.21
MIPI 阻抗控制 – 表层走线 Option2

## Slide 64
MIPI 阻抗控制 – 内层走线
Layer | Target Z (ohm) | W (mils) | S (mils) | Ds (mils) | Dg (mils) | Estimated Z (ohm)
L2/L3 | 100 | 5 | 10 | 12 | 12 | 98.93
Core
GND
W
W
S
Ds
Dg
W
W
S
Dg
pp
GND
P
N
P
N
G
G

## Slide 65
MIPI 阻抗控制 – 内层走线
Target Z (ohm) | W (mils) | S (mils) | Ds (mils) | Dg (mils) | Estimated Z (ohm)
100 +/- 5% | 5 | 10 | 12 | 12 | 98.93
 | 4 | 7 | 12 | 12 | 100.18

## Slide 66
EPHY/USB 阻抗控制 – 内层走线
Core
GND
G
G
P
N
W
W
S
D
D
GND
pp
Layer | Target Z (ohm) | W (mils) | S (mils) | D (mils) | Estimated Z (ohm)
L2/L3 | 100 | 5 | 10 | 12 | 98.92
 | 90 | 5 | 7 | 6 | 90.33

## Slide 67
Target Z (ohm) | W (mils) | S (mils) | D (mils) | Estimated Z (ohm)
100 +/- 5% | 5 | 10 | 12 | 98.92
 | 4 | 7 | 8 | 99.11
Target Z (ohm) | W (mils) | S (mils) | D (mils) | Estimated Z (ohm)
90 +/- 5% | 5 | 7 | 6 | 90.33
 | 4 | 5 | 6 | 90.34
EPHY/USB 阻抗控制 – 内层走线

## Slide 68
Antenna 50ohm 阻抗控制
Layer | Target Z (ohm) | W (mils) | D1 (mils) | D2(mils) | Estimated Z (ohm) | Note
Top | 50 | 30 | 6 | 12 | 50.93 | Ref layer L4
Layer - Top
pp
GND
G
G
Sig
L1
L2
Core
GND
L3
GND
pp
L4
D2
D2
GND
PWR
PWR
W
D1
D1

## Slide 69
Target Z (ohm) | W (mils) | D1 (mils) | D2(mils) | Estimated Z (ohm)
50 +/- 5% | 30 | 6 | 12 | 50.93
Antenna 50ohm 阻抗控制
pp
GND
G
G
Sig
L1
L2
Core
GND
L3
GND
pp
L4
D2
D2
GND
PWR
PWR
W
D1
D1

## Slide 70
MIPI/EPHY/USB/Antenna 阻抗控制
真6层, 6-layer PCB

## Slide 71
MIPI/EPHY/USB 阻抗控制 –表层走线 Option1
MIPI/USB differential signals are required impedance control - Target impedance: (1) MIPI- CSI/DSI: 100ohm (2)USB: 90ohm
Differential signals shielding rule:
- pair to pair GND shielding
pp
GND
G
G
P
N
W
W
S
D
D
Layer | Target Z (ohm) | W (mils) | S (mils) | D (mils) | Estimated Z (ohm)
Top/Bottom | 100 | 5 | 5 | 6 | 97.99
 | 90 | 5 | 4 | 6 | 92.48

## Slide 72
MIPI/EPHY/USB 阻抗控制 –表层走线 Option1
Target Z (ohm) | W (mils) | S (mils) | D (mils) | Estimated Z (ohm)
100 +/- 5% | 5 | 5 | 6 | 97.99
Target Z | W (mils) | S (mils) | D (mils) | Estimated Z (ohm)
90 +/- 5% | 5 | 4 | 6 | 92.48

## Slide 73
MIPI 阻抗控制 – 表层走线 Option2
pp
GND
G
P
N
W
W
S
Ds
Dg
G
P
N
W
W
S
Dg
Layer | Target Z (ohm) | W (mils) | S (mils) | Ds (mils) | Dg (mils) | Estimated Z (ohm) | Rule
Top/Bottom | 100 | 5 | 5 | 12 | 12 | 99.96 | Ds=3W, Dg=3W

## Slide 74
MIPI 阻抗控制 – 表层走线 Option2
Target Z (ohm) | W (mils) | S (mils) | Ds (mils) | Dg (mils) | Estimated Z (ohm)
100 +/- 5% | 5 | 5 | 12 | 12 | 99.96
 | 4 | 4 | 12 | 12 | 101.21

## Slide 75
MIPI 阻抗控制 – 内层走线
Core
GND
W
W
S
Ds
Dg
W
W
S
Dg
pp
GND
P
N
P
N
G
G
Layer | Target Z (ohm) | W (mils) | S (mils) | Ds (mils) | Dg (mils) | Estimated Z (ohm)
L2/L3 | 100 | 5 | 10 | 12 | 12 | 98.44

## Slide 76
MIPI 阻抗控制 – 内层走线
Target Z (ohm) | W (mils) | S (mils) | Ds (mils) | Dg (mils) | Estimated Z (ohm)
100 +/- 5% | 5 | 10 | 12 | 12 | 98.44
 | 4 | 7 | 12 | 12 | 99.92

## Slide 77
EPHY/USB 阻抗控制 – 内层走线
Core
GND
G
G
P
N
W
W
S
D
D
GND
pp
Layer | Target Z (ohm) | W (mils) | S (mils) | D (mils) | Estimated Z (ohm)
L2/L3 | 100 | 5 | 10 | 12 | 98.44
 | 90 | 5 | 7 | 6 | 90.14

## Slide 78
EPHY/USB 阻抗控制 – 内层走线
Target Z (ohm) | W (mils) | S (mils) | D (mils) | Estimated Z (ohm)
100 +/- 5% | 5 | 10 | 12 | 98.44
 | 4 | 7 | 8 | 98.92
Target Z (ohm) | W (mils) | S (mils) | D (mils) | Estimated Z (ohm)
90 +/- 5% | 5 | 7 | 6 | 90.14
 | 4 | 5 | 6 | 90.24

## Slide 79
Antenna 50ohm 阻抗控制
Layer - Top
Layer | Target Z (ohm) | W (mils) | D1 (mils) | D2(mils) | Estimated Z (ohm) | Note
Top | 50 | 30 | 6 | 12 | 50.55 | Ref layer L5
pp
GND
G
G
Sig
W
D1
D1
L1
L2
Core
GND
L3
GND
pp
L4
D2
D2
GND
L5
Core
PWR
PWR
GND
GND

## Slide 80
Target Z (ohm) | W (mils) | D1 (mils) | D2(mils) | Estimated Z (ohm)
50 +/- 5% | 30 | 6 | 12 | 50.55
Antenna 50ohm 阻抗控制
pp
GND
G
G
Sig
W
D1
D1
L1
L2
Core
GND
L3
GND
pp
L4
D2
D2
GND
L5
Core
PWR
PWR
GND
GND